## Slide 1
Laboratory tests

## Slide 2
Objectives
Identify the main causes of outbreak in the work zone
Know the different types of samples and diagnostic tests that can be conducted, based on the infection dynamics
Review the role of the laboratory coordinated with surveillance to characterize outbreaks

## Slide 3
Content
Most frequent etiologies in the Americas
Most commonly used tests for diagnosing etiologic agents
– Serology
– Molecular
– Microscopic
Specimen type, collection, and conservation
– Examples of type of sample and appropriate conservation

## Slide 4
Most common etiologies
in the Americas
Febrile syndrome:
– Dengue, Chikungunya, Zika, yellow fever, influenza, leptospirosis, malaria
Icteric febrile syndrome:
– Yellow fever, leptospirosis, malaria, hepatitis
Hemorrhagic icteric febrile syndrome:
– Yellow fever, leptospirosis
Hemorrhagic febrile syndrome:
– Dengue, yellow fever, leptospirosis, hantavirus
Neurological syndromes:
– Bacterial, viral (Zika and viral encephalitis), polio, botulism
Respiratory syndromes:
– Influenza, hantavirus, diphtheria and other respiratory viruses
Acute diarrheic disease:
– Cholera, rotavirus, norovirus, enterobacteria
Exanthematous disease:
– Zika, measles, rubella

## Slide 5
Most used tests for diagnosing etiologic agents
Serological:
– ELISA (IgM and IgG)
– Direct and indirect immunofluorescence
Molecular:
– Polymerase chain reaction (PCR)
– Real time PCR
– Sequencing
Microscopic:
– Optical microscopy

## Slide 6
Serological tests (Serology)
Two types: direct and indirect tests
– Direct tests: based on the antigen antibody reaction to investigate the presence of antigen. That is, these tests investigate the presence of the etiologic agent or one of its components. Example: direct immunofluorescence.
– Indirect tests: based on detecting specific antibodies against the agent or one of its components, which indirectly allow us to assume that the pathogen being investigated was present in the host at some point
Detect the presence of antibodies
Cheaper than molecular tests
Based on the antigen antibody reaction and constitute a valuable tool in diagnosing infectious disease

## Slide 7
Serological tests (Serology)
Important concepts for interpreting serological results:
Positive IgM is related to a recent infection
Increased antibody titer in paired samples indicates a recent infection
– First sample: negative
– Second sample: antibodies present
– Antibody titer in the second sample > 4x the antibody titer in the first sample
Positive IgG indicates (generally) a past infection

## Slide 8
Types of samples and appropriate collection
Chart: Days of symptoms
| 1 | 3 | 5 | 7 | 9
Series 1 | 0 | 18 | 28 | 37 | 18 | 12 | 8 | 5 | 3 | 1 | 0 | 0
Chart: Antibodies
| 5 | 15 | 5 | 15
Series 1 | 0 | 7 | 1 | 18 | 5 | 4 | 4
Primary infection
Secondary infection
Notes: Stage of infection when the sample is collected. This refers to the stage of infection when the sample is taken.
It is very important that we know what we can find and when we can find what we will detect in the laboratory.
The curve above shows a typical viral load of a person infected with influenza virus. Viral load is present approximately 10 days after the onset of symptoms. However, its concentration drops considerably after 5 days. Due to the high concentration of viruses, the preferable time for sample collection is between the first 2 to 3 days.
The lower curve shows the antibody stimulation curves in a primary and secondary infection. Collection of serum samples for antibody identification should be performed in the first 7 days for the acute sample (first sample in the acute phase of infection) and the second or convalescence phase taken approximately 2 to 3 weeks after the acute phase.

## Slide 9
Serological tests (Serology)
Immunofluorescence
– Immunofluorescence techniques may be applied as techniques to investigate the presence of viral, parasitic, bacterial, or mycotic antigens in clinical samples or antibodies produced against them in the patient’s serum.
ELISA (enzyme-linked immunosorbent assay)
– Immunoenzymatic techniques are tests based on antibody antigen reaction, making it possible to detect the presence of antibodies produced against viral, parasitic, bacterial, or mycotic antigens in clinical specimens in the patient’s serum.
– The ELISA technique may be used to detect IgM or IgG.

## Slide 10
Molecular tests
Are based on detecting the etiologic agent’s genome.
Make it possible to detect the etiologic agent’s RNA or DNA with high sensitivity and specificity.
Are more costly than serology.
Make it possible to confirm the presence of the etiologic agent in clinical samples.
Make it possible to detect RNA or DNA even in very small sample volumes.

## Slide 11
Molecular tests
Polymerase chain reaction (end point PCR)
– The end point PCR is based on amplifying and visualizing the complementary DNA or ADNA (cDNA). This technique consists of amplifying and visualizing a specific DNA fragment from the etiologic agent.
Real time PCR
– Also known as quantitative PCR, this test is a variant of the polymerase chain reaction (PCR).
– Real time PCR makes it possible to amplify and at the same time absolutely quantify specific DNA or cDNA molecules

## Slide 12
Microscopic
Consists of using special instruments such as magnifying glasses and microscopes to magnify the size of structures that are invisible to the naked human eye, such as viruses, bacteria, and parasites.
Microscopic observation is necessary in the field of parasitology.
Modes of observation vary based on strategies employed and range from micrometric to nanometric observation.
Therefore, various types of microscopes are required, such as photonic and electronic (scanning, transmission, and atomic energy).

## Slide 13
Microscopic
Optical microscopy technique allows us to visualize bacteria and parasites simply by examining the sample with a microscope.
For bacteria, a Gram stain (a purple stain) is often performed first. Bacteria is classified as follows:
– Gram positive (appear blue because they retain the Gram stain)
– Gram negative (appear red because they do not capture the stain)
A blood swab is performed to detect parasites found in the blood, such as filariasis, malaria, or babesiosis. For this test, a drop of blood is placed on a microscope slide, stained, and examined under the microscope to visualize the parasite.
Optical microscopy

## Slide 14
Sample type, collection, and conservation
Successful laboratory diagnosis depends on two factors prior to the laboratory phase:
Selecting the type of sample:
It is important to select the correct type of sample, based on clinical material and days since the onset of symptoms, whenever it is possible to obtain a positive result (serologically or molecularly)
Sample quality:
There are three factors that have a direct influence on the quality of the sample to be received by the laboratory:
– Correct collection
– Conservation of the cold chain during transport
– Conservation at the appropriate temperature based on the processing time

## Slide 15
Examples of sample type and appropriate conservation
Dengue, Chikungunya, yellow fever, hantavirus, leptospirosis
Zika, measles, and rubella
Hepatitis
Influenza and other respiratory viruses
Bacterial and viral encephalitis
Rotavirus, norovirus, enterobacteria
Malaria
Meningeal disease

## Slide 16
Dengue, Chikungunya, yellow fever, hantavirus, leptospirosis
Type of sample: serum
Quantity: 3 to 7 mL
Transport medium: no additives
Transport conditions: 2 to 8°C
Conservation: -20°C (up to 1 week) / -70°C (period greater than 1 week)
Laboratory diagnosis:
– 1 to 5 days following onset of symptoms: PCR
– 5 to 10 days following the onset of symptoms: PCR + ELISA IgM

## Slide 17
Zika, measles, and rubella
Type of sample: serum
Quantity: 3 to 7 mL
Transport medium: no additives
Transport conditions: 2 to 8°C
Conservation: -20°C (up to 1 week) / -70°C (period greater than one week)
Laboratory diagnosis:
– 1 to 5 following the onset of symptoms: PCR
– 5 to 10 days following the onset of symptoms: PCR + ELISA IgM

## Slide 18
Zika, measles, and rubella
Type of sample: urine
Quantity: 3 to 7 mL
Transport medium: no additives
Transport conditions: 2 to 8°C
Conservation: -20°C (up to 1 week) / -70°C (period greater than 1 week)
Laboratory diagnosis:
– 1 to 15 days following the onset of symptoms: PCR

## Slide 19
Zika – congenital syndrome or fatal cases
Sample | Quantity | Transport medium | Transport conditions | Conservation >1 week | Laboratory test
Mother’s serum | 5–7 mL | No additives | 4 / 8 °C | -20 / -70 °C | PCR, ELISA IgM, PRNT, others
Umbilical cord blood | 5–7 mL | No additives | 4 / 8 °C | -20 / -70 °C | PCR, ELISA IgM, PRNT, others
Placenta | 0,5–1 mL | Buffered formalin | 4 °C – TA* | 4 °C – TA* | Immunohistochemical
Placenta | 5–7 mL | Saline solution | 4 / 8 °C | -20 / -70 °C | PCR
Umbilical cord (tissue) |  | Buffered formalin | 4 °C – TA* | 4 °C – TA* | Immunohistochemical
Umbilical cord (tissue) |  | Saline solution | 4 / 8 °C | -20 / -70 °C | PCR
Newborn’s blood | 0,5–1 mL | No additives | 4 / 8 °C | -20 / -70 °C | PCR, ELISA IgM, PRNT, others
Newborn’s CSF** | 0,5 mL | No additives | 4 / 8 °C | -20 / -70 °C | PCR, ELISA IgM, PRNT, others
Mother’s total blood | 5–7 mL | EDTA, others | 4 / 8 °C | 4 °C | Biochemical, others
Newborn’s total blood | 2–5 mL | EDTA, others | 4 / 8 °C | 4 °C | Biochemical, others
Tissue** | 3x3 cm (approx) | Buffered formalin | 4 °C – TA* | 4 °C | Immunohistochemical
Tissue** | 3x3 cm (approx) | Saline solution | 4 / 8 °C | -20 / -70 °C | PCR
* Ambient temperature
** Under medical indication for suspected neurological syndrome
*** Fatal cases: brain, liver, kidney, others

## Slide 20
Hepatitis
Type of sample: serum
Quantity: 3 to 7 mL
Transport medium: no additives
Transport conditions: 2 to 8°C
Conservation: -20°C (up to 1 week) / -70°C (period greater than 1 week)
Laboratory diagnosis:
– 1 to 5 days after onset of symptoms: PCR + Elisa HBsAg
– 5 to 10 after onset of symptoms: PCR + ELISA IgM

## Slide 21
Influenza and other respiratory viruses
Type of sample: nasopharyngeal swab
Quantity: 2 nylon swabs
Transport medium: viral transport medium or saline solution (3 mL)
Transport conditions: 2 to 8°C
Conservation: 4°C until aliquots are prepared; aliquots to a -20°C (up to 48 hours) and -70°C (period greater than 48 hours)
Laboratory diagnosis:
– PCR or IF (only typification) followed by PCR

## Slide 22
Influenza and other respiratory viruses
Type of sample: nasopharyngeal aspiration; nasopharyngeal wash
Material: suction device
Transport medium: saline solution
Transport conditions: 2 to 8°C
Conservation: 4°C until aliquots are prepared; aliquots to a -20°C (up to 48 hours) and -70°C (period greater than 48 hours)
Laboratory diagnosis:
– PCR or IF (only typification) followed by PCR

## Slide 23
Bacterial and viral encephalitis
Type of sample: serum
Quantity: 3 to 7 mL
Transport medium: no additives
Transport conditions: 2 to 8°C
Conservation: -20°C (up to 1 week) / -70°C (period greater than 1 week)
Laboratory diagnosis:
– 1 to 5 following onset of symptoms: PCR
– 5 to 10 following onset of symptoms: PCR + ELISA IgM

## Slide 24
Bacterial and viral encephalitis
Type of sample: blood
Quantity: 3 to 7 mL
Transport medium: no additives
Transport conditions: 2 to 8°C
Conservation: -20°C (up to 1 week) / -70°C (period greater than 1 week)
Laboratory diagnosis:
– 1 to 5 following onset of symptoms: PCR
– 5 to 10 following onset of symptoms: PCR + ELISA IgM

## Slide 25
Rotavirus, norovirus, enterobacteria
Type of sample: fecal material
Conservation: 2 to 8°C
Laboratory diagnosis:
– Generally, molecular methods are used based on PCR and ELISA kits for antigen detection

## Slide 26
Malaria
Type of sample: total blood
Conservation: 2 to 4°C
Laboratory diagnosis:
– Large drop (extended) for microscopy

## Slide 27
Meningeal disease
Bacteria culture
Hemoculture
PCR
Viral isolation in cell culture

## Slide 28
© Pan American Health Organization, 2023
Property of the Pan American Health Organization. Reproduced with permission pursuant to the Creative Commons Attribution-NonCommercial-NoDerivs 3.0 IGO license (CC BY-NC-ND 3.0 IGO).
In any use of this work, there should be no suggestion that the Pan American Health Organization (PAHO) endorses any specific organization, product, or service. Use of the PAHO logo, in a way that is not already incorporated in the work or consistent with the Creative Commons license CC BY-NC-ND 3.0 IGO, is strictly prohibited. Any use of this work that is inconsistent with or not permitted under the Creative Commons license BY-NC-ND 3.0 IGO requires the express written consent of PAHO.
Further, all reasonable precautions have been taken by PAHO and the GS/OAS to verify the information contained in this publication. However, the published material is being distributed without warranty of any kind, either expressed or implied. The responsibility for the interpretation and use of the material lies with the reader. In no event shall PAHO and/or the OAS or GS/OAS be liable for damages arising from its use